## Slide 1: Image Stabilization
Techniques that reduce blurring associated with modest motion of a camera

## Slide 2: Camera Shake
Camera shake is the thief of sharpness!
If you are hand-holding a camera and lens, they will move as you press the shutter release.
Movement during exposure blurs the image.

## Slide 3: Image Blur
Movement of the camera during exposure will result in image blur.

## Slide 4: Camera Shake
The best way to avoid camera shake is to use a sturdy tripod!
However, it is not always practical, permissible or convenient to use a tripod.
It is impossible to hold a camera absolutely still, so some movement will occur during the exposure period.
The longer the focal length of the lens the greater the effect of camera shake.

## Slide 5: Tripod

## Slide 6: Shutter Speed
Fast shutter speeds will minimise image blur ( e.g. 1/1000 sec) due to camera shake.
Slow shutter speeds (e.g. 1/30 sec) will maximise image blur due to camera shake.
Image blur due to camera shake increases as the focal length of the lens increases.
Wide angle lenses (with relatively short focal lengths) exhibit less image blur problems than telephoto lenses (with long focal lengths).

## Slide 7: Applications in still photography
In photography, image stabilization can facilitate shutter speeds 2 – 5 stops slower than non stabilized exposures.
For example: 1/250  1/8 sec (5 stops)
That is, exposures can be 4 – 32 times longer without incurring noticeable blur.
This is a great advantage in low-light conditions or when using telephoto lenses.

## Slide 8: ISO
By using slow shutter speeds we can avoid using high ISO settings.
The higher the ISO setting, the more noise will appear in an image.

## Slide 9: The Reciprocal Rule
The old rule of thumb for determining the slowest shutter speeds possible for hand holding without noticeable blur due to camera shake is: 1/focal length of the lens (mm)
For a 50mm lens, this would be: 1/50 sec
This rule was based on the 35mm film camera
You can’t apply this rule to digital cameras without taking into account various factors.

## Slide 10: Crop Factor (1)
35mm film cameras produce negative images that are 36 x 24mm in size
This size has become an industry standard and is know known as “full frame”.
Full frame digital cameras have sensors that cover this particular image area.
However, until fairly recently, sensors of this size were very expensive.

## Slide 11: Digital Sensor

## Slide 12: Crop Factor (2)
Camera manufacturers have in the past and continue to produced a range of digital cameras with smaller sensors than full frame.
The advantages are:
1) It keeps the cost down;
2) It facilitates smaller camera bodies and lenses – hence less weight and bulk.

## Slide 13: Sensor Sizes

## Slide 14: Crop Factor
The Crop Factor is the ratio of the dimensions of a camera’s imaging area compared to a reference format.
In the case of digital cameras the reference is the 35mm film camera’s imaging area.
35 x 24mm = 840 mm2

## Slide 15: The outer red box displays what a 36 x 24 mm sensor would see. The inner blue box displays what a 15 x 23 mm sensor would see using the same lens.

## Slide 16: Crop Factor
Sensors with a smaller imaging area than the standard (36 x 24mm) will see a smaller area of the image projected by the lens.
In other words, the image will be cropped compared to that of a full frame sensor.

## Slide 17: Crop Factor of common cameras
Multiplying a lens focal length by the crop factor gives the equivalent focal length of a lens that would yield the same field of view if used on a full frame (FF) camera.
Full frame: 1
APS-C: 1.5 or 1.6 (Canon)
Micro 4/3 (Olympus, Panasonic): 1.84 – 2
1” sensor: 2.7
1/2.3” (compacts): 5.6
iPhone 6: 7.21 (equivalent to a 28mm FF lens)

## Slide 18: Reciprocal Rule and Crop Factor
Multiple the focal length of the lens by the crop factor to obtain the equivalent focal length.
An APS-C 35mm lens is equivalent to:
1.5 x 35mm = 52.5mm full frame lens
An micro 4/3 25mm lens is equivalent to:
2 x 25mm = 50mm full frame lens
An APS-C 16mm lens is equivalent to a 1.5 x 16mm = 24mm full frame lens.

## Slide 19: Practical considerations
The reciprocal rule suggests that if I was to use an APS-C 35mm lens I should not use a shutter speed of less that 1/50 sec (say 1/60 sec) to avoid image blur.
What about an APS-C 200mm lens?
200 x 1.5 = 1/300 sec

## Slide 20: Digital Cameras
Image blur may well be more apparent with modern digital cameras than it was with 35mm film cameras.
Sensors with 24MP are now common.
Pro cameras may have 40 - 50MP sensors.
This suggests that if we display these high resolution images on a large scale we may have to use even higher shutter speeds to retain tack sharpness!

## Slide 21: Sensor Sizes

## Slide 22: Sensor Sizes

## Slide 23: Sensor Sizes

## Slide 24: Sensor Sizes

## Slide 25: Sensor Sizes

## Slide 26: Sensor Sizes

## Slide 27: Smartphone Sensors

## Slide 28: Image Stabilization
There are two major types of implementation:
Optical Image Stabilization (OIS, IS or OS)
In-body Image Stabilization (IBIS)
Because cameras are a three dimensional tool, image stabilization needs to work on up to six different planes to properly correct camera movement.

## Slide 29: Camera Movements

## Slide 30: Camera Movements

## Slide 31: Camera Movements

## Slide 32: Optical Image Stabilization (O.I.S.)
Lens stabilization employs a floating lens element.
This lens is controlled electronically by a microcomputer within the lens and shifts in the opposite direction of the camera shake, helping to stabilize the image.
This is detected in microseconds and can give up to 5-stops of stabilization.
OIS is by far the most common type of IS.

## Slide 33: Floating Lens

## Slide 34: IOS

## Slide 35: IOS

## Slide 36: IOS mechanism
To deliver this performance, the lens uses a high precision gyro(s) sensor.
A linear motor technology checks for camera shake 8000 times a second and controls location feedback of the corrective optical system 1600 times a second to counter even the most minute of high frequency camera shakes (Fujifilm).

## Slide 37: OIS in a Fujinon lens

## Slide 38: Lens Stabilization

## Slide 39: No IOS at 1/13 sec. with 400mm lens

## Slide 40: IOS on at 1/13 sec. 400mm

## Slide 41: Panning
Panning is a technique used to get a sharp subject against a motion blurred background.

## Slide 42: Panning
A problem arises when the camera IOS system can’t distinguish between your deliberate panning motion and unintentional camera shake.
Some recent cameras can detect when you’re panning.

## Slide 43: In-Camera Stabilization (IBIS)
IBIS works by moving the sensor inside the camera in order to compensate for the camera movement.
IBIS has a floating sensor controlled by electromagnets.
Built-in accelerometers measure lateral motion, correcting the sensor by moving it left/right and up/down.
Some recent cameras also have gyroscopes built-in to detect rotational movement.

## Slide 44: Five-Axis IBIS

## Slide 45: IBIS
Therefore, five-axis image stabilization can be achieved: horizontal, vertical, yaw, pitch and roll.

## Slide 46: Five Axis IBIS

## Slide 47: Advantages to In-Lens Stabilization
It is far more effective in telephoto lenses.
It works better in low light conditions
Has no effect on metering and autofocus
Will offer better battery life than IBIS

## Slide 48: Advantages to In-Body Stabilization
Generally, IBIS is cheaper in the long run if you wish to own a range of lenses (particularly primes).
IBIS is universal – it works with all lenses.
IBIS operates in silence – useful for video.
IBIS offers cleaner bokeh
Vloggers benefit from more stable footage.

## Slide 49: IOS and IBIS working together
Manufacturers like Olympus, Panasonic (Lumix), Fuji and Sony have a list of their IOS lenses that can be used alongside IBIS so that they work in conjunction.
For instance, IBIS deals with 3-axis stabilization while IOS deals with pitch and yaw.

## Slide 50: Fuji Lenses

## Slide 51: Fuji Range of Lenses

## Slide 52: Motion Blur and Image Stabilization
Image Stabilization does NOT eliminate blur due to a subject moving during exposure.
Using slow shutter speeds will result in motion blur.

## Slide 53: Motion Blur at 1/13 sec

## Slide 54: Motion Blur at 1/13 sec.

## Slide 55: Intentional Camera Movement (ICM)
60mm lens at 1/8 sec

## Slide 56: Lenses used in testing
Fuji Lens Equivalent Reciprocity
14mm 21mm 1/21 sec
35mm 52.5mm 1/52.5 sec
56mm 84mm 1/85 sec
55mm* 82.5mm 1/82.5 sec
200mm* 300mm 1/30 sec
* ISO lenses